## Slide 1
SYSTEM ARCHITECTURE
Four-phase data pipeline
PHASE 1
Rank candidates
EPA ECHO / ICIS-NPDES DMR → active POTWs, flow features, composite score
17,158 ranked
PHASE 2
Estimate energy
Monte-Carlo hydropower physics over each site's flow-duration curve
5,468 retained
PHASE 3
Size turbine
USGS 3DEP head + H–Q turbine selection + rated-power optimizer
3,783 viable
PHASE 4
Score economics
CapEx/OpEx cost model → NPV, IRR, payback, LCOE scorecard
1,141 ready
Data flows left → right. Each phase reads the prior phase's versioned parquet and appends new columns. The site count falls at each stage as physical data requirements (flow → head → power → economics) are applied. Core physics constant throughout: P = η × ρ × g × Q × H.
WOWERS — Waste Outfall Water Energy Recovery System
01
Notes: [SYSTEM ARCHITECTURE — the four phases]
This is the map of the whole system. Four phases, left to right, and each one feeds the next.
Phase 1 ranks every plant from the raw EPA flow data. Phase 2 estimates how much energy each site could generate using hydropower physics. Phase 3 finds the real elevation drop and sizes an actual turbine. Phase 4 scores the economics — the financial scorecard.
The mechanics: each phase reads the previous phase's output file — we use "parquet," which is just an efficient columnar data file format — and appends new columns. So nothing is hidden; any number I show you later traces back to a specific column in a specific file.
Notice the counts in the colored chips at the bottom of each card — 17,158, then 5,468, then 3,783, then 1,141. The number falls at every stage. That's by design: each phase adds a stricter physical requirement — first you need usable flow, then you need a real elevation drop, then enough power to be worth a turbine, then the economics have to work. We'll dig into exactly why each drop happens.
And the constant running through the entire pipeline is the standard hydropower equation at the bottom: power equals efficiency times water density times gravity times flow times head. Everything else is built around that.

## Slide 2
DATA PROVENANCE
Every input is public & free
Dataset | Provider | What it gives us | Used in
EPA ECHO / ICIS-NPDES DMR | US EPA | Measured monthly effluent flow (param 50050, MGD) per outfall, FY2009–24 | Phase 1–2
NPDES facility registry | US EPA | Active POTW list: permit status, type, design flow, lat/lon | Phase 1
NPDES outfall coordinates | US EPA | Per-outfall lat/lon (626k features) for precise elevation lookup | Phase 3
USGS 3DEP elevation (EPQS) | USGS | Ground elevation at facility & outfall → gross head | Phase 3
State industrial electricity rates | EIA (2023) | $/kWh by state (51 entries) for revenue | Phase 4
Turbine manufacturer database | Vendor sites | 15 turbines: flow/head envelope, $/kW band, WW-certified | Phase 3–4
All sources are public. Backbone = EPA DMR (~279M rows). Acquisition: bulk ZIP per fiscal year from echo.epa.gov; elevation via live USGS EPQS API with on-disk caching.
WOWERS — Waste Outfall Water Energy Recovery System
02
Notes: [DATA PROVENANCE — where every number comes from]
This is the "is this real, or did you make it up?" slide. The answer: every single input is a free, public, government or manufacturer source. No paywalls, no proprietary feeds.
Going down the table. The backbone is the EPA DMR data — those Discharge Monitoring Reports — which give us measured monthly effluent flow, in million gallons per day, for every outfall. The NPDES registry — NPDES is the federal wastewater permit program — gives us the master list of active plants with their permit status and location. A separate EPA outfall file gives us precise latitude and longitude for each discharge point. USGS 3DEP is the US Geological Survey's 3-D Elevation Program; we query it through an API called EPQS to get ground elevation, which is how we compute head. State electricity rates from the Energy Information Administration give us dollars per kilowatt-hour for revenue. A turbine manufacturer database — fifteen real turbines with their flow and head limits and published cost per kilowatt — anchors our cost model.
The takeaway: this is built entirely on data taxpayers already paid for.

## Slide 3
DATA DEEP-DIVE
EPA DMR — the flow backbone
▸ What it is: the Discharge Monitoring Report database — every NPDES-permitted facility's legally-required self-reported measurements, published quarterly by EPA ECHO (free bulk download).
▸ Scale ingested: ~279 million raw rows, fiscal years 2009–2024, all 50 states + territories (~10 GB compressed).
▸ What we extract: flow parameter code 50050 (effluent flow, MGD). All other pollutant parameters are discarded for this use.
▸ Engineering done to make it usable:
  – Filter to active POTWs only (permit status EFF/NON/ADC; exclude federal facilities).
  – Parse + normalize units, handle NODI no-data codes (below-detection → 0, estimated, missing).
  – Collapse to a monthly flow time series → 20,020,548 clean rows.
  – Null physically impossible readings: a per-reading cap (2,000 MGD) and a 5×-design-flow guard removed 459 unit-error artifacts (e.g. a high school reporting 585 MGD).
DMR BY THE NUMBERS
~279 M
raw DMR rows ingested
16
fiscal years (2009–2024)
20.0 M
clean monthly-flow rows
17,158
active POTWs retained
459
unit-error rows nulled
WOWERS — Waste Outfall Water Energy Recovery System
03
Notes: [DATA DEEP-DIVE — the EPA DMR backbone]
Let me spend a minute on the single most important and most labor-intensive dataset, because it's the foundation of everything.
The DMR database — the Discharge Monitoring Reports — is what every regulated facility in the country is legally required to file with EPA. We pulled sixteen fiscal years of it, 2009 through 2024. Raw, that's about 279 million rows and roughly ten gigabytes — every pollutant measurement for every outfall.
We don't need most of it. We extract just one thing: the flow parameter, EPA code 50050, measured in million gallons per day — "MGD." That's the water volume we can run a turbine on.
Then the engineering — and this is the hard part. We filter to active municipal plants only. We handle the messy "no-data" codes EPA uses — for example, a "below-detection" reading becomes zero, an "estimated" flag is tracked separately. We collapse the whole thing into a clean monthly flow time series — that's 20 million clean rows out of the 279 million raw. And critically, we scrub physically impossible readings: a per-reading cap and a guard that nulls any value more than five times a plant's design capacity. That one rule caught 459 unit-error rows — for instance a high school reporting 585 million gallons a day, which is obviously a data-entry mistake. The panel on the right is just those numbers at a glance. Bottom line: this is real, audited engineering, not a spreadsheet estimate.

## Slide 4
PHASE 1 · METHOD
Rank candidate plants from flow data
▸ Per-facility flow features computed from the monthly time series: mean / median flow, coefficient of variation (consistency), P10–P90 percentiles, a 20-point flow-duration curve (FDC), utilization ratio (actual ÷ design flow), and years of data.
▸ Each feature is min-max normalized to [0,1] across all facilities (variability and CV are inverted — steadier is better).
▸ Composite score = weighted sum (weights re-normalized to sum to 1):
Ranking component | Weight | Rationale
Mean flow | 0.35 | More water → more power potential
P10 flow (reliable baseline) | 0.20 | Firm flow available ≥90% of the time
Flow consistency (1 − CV) | 0.20 | Steady flow → higher capacity factor
Utilization ratio | 0.15 | Plant running near its design capacity
Data quality (years of record) | 0.10 | Confidence in the estimate
ASSUMPTIONS
• Weights are expert-set, not learned (transparent & tunable in config).
• Min-max scaling makes scores relative to the national cohort.
• Sites with design_flow = 0 (industrial misclassification) forced to score 0.
WOWERS — Waste Outfall Water Energy Recovery System
04
Notes: [PHASE 1 · METHOD — ranking]
Phase 1's job is to turn raw flow into one priority score per plant, zero to one, so we know where to look first.
From each plant's monthly flow time series we compute statistical features. Mean and median flow — the typical volume. The coefficient of variation, or CV — that's the standard deviation divided by the mean, a measure of how bumpy the flow is; lower is steadier. The P10 through P90 percentiles — "P10" means the flow level that the plant exceeds 90% of the time, so it's a conservative, reliable baseline; "P90" is the high end. A twenty-point flow-duration curve, which I'll explain more in Phase 2 — it's basically the full profile of how often each flow level occurs. Utilization ratio — actual flow divided by the plant's permitted design capacity. And years of data, as a confidence proxy.
Every feature is "min-max normalized" — rescaled so the smallest value across all plants becomes zero and the largest becomes one — so we can combine different units fairly. For the bumpiness measures we invert them, because steadier should score higher.
The composite score is just a weighted sum, and the weights are in the table. We weight mean flow highest at 35%, then reliable baseline flow and consistency at 20% each, utilization 15%, data quality 10%.
The assumptions box is the honest part: these weights are expert-set, not machine-learned — which makes them transparent and easy for you to challenge or tune. And anything reporting zero design flow, a sign of an industrial misclassification, is forced to score zero.

## Slide 5
PHASE 1 · RESULTS
17,158 POTWs ranked — top 10
# | Facility | State | Mean flow (MGD) | Score
1 | D.C. WASA (Blue Plains) | DC | 304.1 | 0.603
2 | Passaic Valley Sewerage Comm. | NJ | 246.2 | 0.525
3 | ALCOSAN Sewer System | PA | 193.9 | 0.525
4 | MWRDGC Stickney WRP | IL | 1,200.0 | 0.513
5 | NYCDEP — Ward's Island WRRF | NY | 206.9 | 0.507
6 | NYCDEP — Newtown Creek WRRF | NY | 203.1 | 0.503
7 | Phila. Water Dept — NE WPC Plant | PA | 172.8 | 0.489
8 | Central Regional WWTP | TX | 182.9 | 0.477
9 | Robert W. Hite Treatment Facility | CO | 131.4 | 0.465
10 | Plover WWTF | WI | 1.4 | 0.439
Reads correctly: the largest metros lead, but Plover WI (#10, 1.4 MGD) ranks high on flow consistency + data quality — the score is not just a flow sort. Output file: phase1/ranked_candidates.parquet (17,158 × 33).
WOWERS — Waste Outfall Water Energy Recovery System
05
Notes: [PHASE 1 · RESULTS — the ranked list]
Here's the output: all 17,158 plants ranked, and the top ten on screen.
The "Score" column is that zero-to-one composite score from the previous slide. "MGD" is million gallons per day — average flow.
A sanity check is the most useful thing here. The top of the list is exactly who you'd expect — the country's biggest metropolitan wastewater plants. DC's Blue Plains. Passaic Valley in New Jersey. Chicago's Stickney plant, which at 1,200 million gallons a day is the single largest wastewater plant in the United States. New York City's plants. So the ranking is behaving sensibly on the high end.
But look at number ten — Plover, Wisconsin, with only 1.4 million gallons a day. It's a tiny plant, yet it ranks in the top ten. Why? Because its flow is extremely steady and very well documented, and our scoring rewards consistency and data quality, not just raw size. That's the proof the score is doing something smarter than a simple flow sort — it's finding reliable sites, not just big ones.
Everything here comes out of one file, ranked_candidates.parquet, 17,158 rows by 33 columns. If you ever want to audit a specific plant, it's one row in that file.

## Slide 6
PHASE 2 · METHOD
Monte-Carlo energy estimation
P (kW) = η × ρ × g × Q × H ÷ 1000 (η = efficiency, ρ = 998.2 kg/m³, g = 9.81 m/s², Q = flow m³/s, H = head m)
▸ Per plant, 10,000 Monte-Carlo iterations. Each iteration samples three uncertain inputs from triangular distributions:
  – Head H — from a size-based literature range (see table; replaced by real elevation in Phase 3).
  – Efficiency η — Triangular(0.70, 0.82, 0.90).
  – Availability — Triangular(0.90, 0.95, 0.98).
▸ Within each iteration, power is integrated across the 20-point flow-duration curve by the trapezoidal rule × 8,766 h/yr × availability → annual kWh. This captures that flow varies through the year, not just the mean.
▸ Output per site: energy P10 / P50 / P90, mean, std, P50 power (kW), capacity factor.
Archetype | Head low / mode / high (m)
Large POTW (>10 MGD) | 3 / 8 / 15
Medium POTW (1–10 MGD) | 2 / 5 / 10
Small POTW (<1 MGD) | 1 / 3 / 6
KEY ASSUMPTIONS
• Head ranges are literature-derived by plant size (no site elevation yet).
• FDC tail truncation underestimates energy by ~2–3% — conservative for screening.
• Same physics constants shared with Phase 3 (single source of truth in config).
WOWERS — Waste Outfall Water Energy Recovery System
06
Notes: [PHASE 2 · METHOD — Monte Carlo energy]
Phase 2 answers: how many kilowatt-hours per year could each plant actually generate?
The physics is the textbook hydropower equation in the dark band: power in kilowatts equals efficiency, times water density (about 998 kilograms per cubic meter), times gravity (9.81), times flow Q in cubic meters per second, times head H in meters, divided by a thousand. Efficiency — the Greek letter eta — is the fraction of the water's energy the turbine captures. Head, again, is the vertical drop.
Now, rather than plug in single guesses, we run a "Monte Carlo" simulation. That just means: instead of one calculation, we run ten thousand per plant, each time drawing the uncertain inputs randomly from a realistic range, so we get a distribution of outcomes instead of one fragile number. The three uncertain inputs each use a "triangular distribution" — a simple shape defined by a low, a most-likely, and a high value. Head varies by plant size from the literature table on the right. Efficiency varies from 0.70 to 0.82 to 0.90. Availability — the fraction of the year the turbine is actually running — varies from 0.90 to 0.98.
Inside each run, we integrate power across the flow-duration curve using the trapezoidal rule — that's just the standard way to compute the area under a curve — multiplied by the hours in a year. This captures that flow changes through the seasons.
The assumptions, stated plainly: head is still a literature estimate here because we don't have site elevation yet — Phase 3 fixes that. And we knowingly underestimate by two to three percent by clipping the curve's tails, which is conservative.

## Slide 7
PHASE 2 · RESULTS
National energy potential — and DOE cross-check
445 GWh
national P10 (conservative)
699 GWh
national P50 (central)
1,002 GWh
national P90 (optimistic)
▸ Independent validation: DOE estimates US wastewater hydro potential at 500–5,000 GWh/yr. Our P50 of 699 GWh/yr sits inside that band — the model is calibrated against an external authority, not self-referential.
▸ 5,468 sites carried forward with a real energy estimate; 11,690 excluded here — but only because EPA DMR had no usable flow record for them (data gap, not a model rejection).
▸ Top single-site P50 example: MWRDGC Stickney WRP (IL) — ~29 GWh/yr at 1,200 MGD, consistent with its scale.
▸ The probabilistic output (P10/P50/P90) flows into Phase 4 as a built-in sensitivity band — we never bet the financials on one point estimate.
Output file: phase2/energy_yield_estimates.parquet (17,158 rows; 5,468 with estimates, 11,690 flagged excluded).
WOWERS — Waste Outfall Water Energy Recovery System
07
Notes: [PHASE 2 · RESULTS — national energy and the key validation]
Here's the headline energy result and, honestly, the most important validation in the entire project.
First, what P10, P50, and P90 mean, because they're on the cards. These are percentiles of the Monte Carlo output. P50 is the median — the central, most-likely estimate. P10 is the conservative end — there's a 90% chance the real number is at least this high. P90 is the optimistic end. So our national estimate is a band: a central 699 gigawatt-hours per year, with a conservative-to-optimistic range of 445 to 1,002.
Now the validation. The US Department of Energy has independently estimated the hydropower potential of the wastewater sector at 500 to 5,000 gigawatt-hours per year. Our number — derived completely independently, from the bottom up, plant by plant — lands squarely inside that range. That's strong evidence our physics is calibrated against an outside authority, not just internally consistent. If a director asks "how do I know your energy numbers aren't made up," this is the answer.
Two more points. 5,468 sites carried forward with a real energy estimate; the 11,690 that dropped here did so only because EPA had no usable flow record for them — that's a data gap, not us rejecting them. And the probabilistic output flows straight into the financials as a built-in sensitivity band, so we never bet the economics on a single point estimate.

## Slide 8
PHASE 3 · METHOD (HEAD)
Real elevation-based net head
▸ Gross head = facility elevation − outfall elevation, from USGS 3DEP (queried at real per-outfall coordinates from the EPA NPDES outfall layer).
▸ Net head = gross head × (1 − 0.15) — the 15% accounts for pipe friction, valves, bends, and screen losses in the effluent conduit.
▸ Source priority (graceful degradation): real 3DEP elevation → Phase-2 literature head → 5 m design fallback.
▸ Plausibility / divergence gate: a 3DEP head is rejected if it differs from the literature value by more than 4× (catches the API returning a wrong point); negative head (outfall above facility) is physically impossible → rejected.
▸ A genuinely low but valid 3DEP reading (below the 1 m minimum) is trusted and marked non-viable — not overwritten with an optimistic default.
HEAD RESULTS
3,780
sites with real 3DEP head
1,688
fell back to literature head
4,864
sites with valid net head
604
dropped — no valid head
4.7 m
median net head (P10 2.6 / P90 11.0)
WOWERS — Waste Outfall Water Energy Recovery System
08
Notes: [PHASE 3 · METHOD (HEAD) — real elevation]
Phase 3 has two parts. Part one: replace the literature head guess with real terrain data — this is a big credibility upgrade.
Remember head is the vertical drop driving the turbine. Up to now it was an assumption by plant size. Here we compute it for real. Using the outfall's actual coordinates, we query the USGS 3DEP elevation service — the US Geological Survey's national elevation model — for the ground height at the plant and at the discharge point. The difference is "gross head," the raw drop. We then multiply by 0.85 — subtracting a 15% "head loss fraction" for friction, valves, and bends in the pipe — to get "net head," the usable drop.
We don't blindly trust the API, though. There's a priority order: use real 3DEP elevation first; if that's missing, fall back to the literature value; only as a last resort use a five-meter default. And there's a plausibility gate — if the elevation-derived head disagrees with the literature value by more than a factor of four, or if it comes out negative (which would mean the outfall is uphill, physically impossible), we reject that point and fall back. If the real reading is genuinely low — below our one-meter minimum — we trust it and mark the site non-viable rather than overwriting it with an optimistic default. That's the conservative choice.
Results on the right: 3,780 sites got real elevation-based head; 1,688 fell back to literature; 4,864 ended with a valid net head; 604 were dropped for no valid head. Median net head is about 4.7 meters.

## Slide 9
PHASE 3 · METHOD (TURBINE)
Type selection + rated-power optimizer
▸ Turbine type from the standard H–Q envelope: Pelton (H>50 m, low Q) · Francis (H≥10 m) · Crossflow (2–10 m, low Q) · Kaplan (2–10 m, high Q) · in-conduit micro (H<2 m).
▸ Rated-power optimizer: sweep Q_rated = 30…100% of design flow; for each, integrate the part-load efficiency curve η(Q/Q_rated) over the FDC; pick the size that maximizes annual MWh subject to capacity factor ≥ 0.40.
▸ Part-load efficiency η(q) curves are empirical fits to published manufacturer hill charts (Kaplan peaks ~0.93, Francis ~0.91, Pelton 0.88, Crossflow 0.82, micro 0.75).
▸ Each site is matched to a real manufacturer (preferring wastewater-certified, then lowest $/kW) from a 15-turbine vendor database.
▸ Viability floor: rated power must be ≥ 1 kW — 1,081 sites fail this physics floor and are dropped (not an economic rejection).
Turbine type | Sites | Avg kW
Crossflow | 2,771 | 5.0
Francis | 452 | 44.9
Kaplan | 364 | 107.2
In-conduit micro | 196 | 5.4
Total viable | 3,783 | —
ASSUMPTIONS
• Efficiency curves are literature/vendor fits, not site-measured.
• Min capacity factor 0.40; min viable power 1 kW.
• Most sites are small (Crossflow, ~5 kW); energy is concentrated in few large Kaplan/Francis sites.
WOWERS — Waste Outfall Water Energy Recovery System
09
Notes: [PHASE 3 · METHOD (TURBINE) — selecting and sizing]
Part two of Phase 3: now that we have real head and flow, we pick and size an actual turbine.
First, the type. There's a standard "H–Q envelope" — head versus flow — that engineers use to choose a turbine. High head with low flow calls for a Pelton wheel. Medium head, a Francis turbine. Low head with high flow, a Kaplan. Low head with modest flow, a Crossflow — that's the Ossberger or CINK style. And the very lowest head gets an in-conduit micro-turbine that drops inside the pipe. The rules are on the slide.
Then we size it. An optimizer sweeps the turbine's rated flow from 30% up to 100% of the plant's design flow. For each candidate size it integrates the turbine's "part-load efficiency curve" across the flow-duration curve. Part-load efficiency just means a turbine isn't equally efficient at all flows — these curves are empirical fits to manufacturers' published "hill charts," their efficiency maps. It picks the size that maximizes annual energy while keeping the "capacity factor" — actual output divided by theoretical maximum — at or above 0.40.
Each site is then matched to a real manufacturer, preferring ones certified for wastewater and then lowest cost.
One viability floor: rated power must be at least one kilowatt. 1,081 sites fall below that — too tiny to be worth a turbine — and are dropped. That's a physics floor, not an economic rejection.
The result, in the table: 3,783 viable sites. Most are small Crossflow units around five kilowatts, but the energy is concentrated in a few large Kaplan and Francis sites.

## Slide 10
PHASE 4 · METHOD (COST)
CapEx / OpEx model
▸ Equipment $/kW = clamp( A × kW^B , vendor_min , vendor_max ), per turbine type. Power-law from DOE Hydropower Vision + ORNL TM-2014/525, then clamped to real vendor bands.
▸ Vendor-band guardrail: every site's modeled $/kW is cross-checked against manufacturer-published ranges. 0 of 3,783 sites fall outside the band.
▸ Total project CapEx = Equipment + Installation + Interconnection + Permitting:
  – Installation = 17.5% of equipment (mechanical labor only; the director's 15–20% lever; civil works excluded).
  – Interconnection = tiered $50k–$200k by kW; behind-the-meter micro (≤25 kW) only $5k (no grid export).
  – Permitting = tiered: $5k qualifying conduit facility (≤25 kW) → $75k abbreviated FERC → $150k full NEPA.
▸ O&M = fixed % of equipment CapEx per type (1.5–3.0%); one-time costs (install/intercon/permit) are not O&M-bearing.
Type | A | B | $/kW band
Kaplan | 9,500 | -0.35 | 800–10,000
Francis | 8,500 | -0.32 | 1,800–9,000
Pelton | 7,000 | -0.30 | 600–8,000
In-conduit | 20,283 | -0.181 | 2,000–15,000
Crossflow | 7,500 | -0.28 | 500–6,000
WHY 17.5% (not 2–5×)?
Literature “total installed = 2–5× equipment” bundles civil + interconnection + permitting + contingency. We model those as separate explicit lines, so our installation line is mechanical labor ONLY — hence far smaller. Real install quotes are unobtainable (gov procurement opacity), so % of equipment is the defensible proxy.
WOWERS — Waste Outfall Water Energy Recovery System
10
Notes: [PHASE 4 · METHOD (COST) — what it costs to build]
Phase 4 is the money. Part one is the cost model — what it costs to build each site.
"CapEx" is capital expenditure, the upfront build cost. "OpEx" is operating expenditure, the annual running cost. We model equipment cost with a "power law": cost per kilowatt equals a coefficient A times the kilowatt rating raised to a negative exponent B. In plain terms, small turbines cost a lot more per kilowatt than big ones — there's no economy of scale at the bottom. Those coefficients come from Department of Energy and Oak Ridge National Lab cost studies.
The critical guardrail: we then hard-clamp every cost to the real price band that manufacturers actually publish. So the model can never quote a price below or above what a real vendor charges. We cross-checked this — zero of 3,783 sites land outside the vendor band.
On top of equipment we add three real "balance-of-system" lines — that just means everything besides the turbine itself. Installation is mechanical labor, modeled at 17.5% of equipment cost — that's your lever, and I'll come back to it. Interconnection is the grid hookup, tiered fifty to two hundred thousand dollars by size; tiny behind-the-meter sites that don't export to the grid only pay five thousand. Permitting is tiered by FERC small-hydro practice — FERC is the Federal Energy Regulatory Commission — from five thousand for a simple conduit exemption up to a hundred fifty thousand for a full federal environmental review.
The box on the right explains why our 17.5% install looks small versus the literature's "two-to-five-times" rule: that rule bundles civil works, interconnection, and permitting together — but we already model those as separate explicit lines, so our install figure is mechanical labor only.

## Slide 11
PHASE 4 · METHOD (FINANCE)
30-year DCF scorecard
Revenueₜ = Energyₜ × (state $/kWh + REC $0.01) ; Energyₜ = E₁ × (1 − 0.002)^(t−1)
NPV = −CapEx + Σ (Revenueₜ − OpEx) / (1 + 0.06)^t over t = 1…30 yr
IRR = discount rate where NPV = 0 (Brent solver) · LCOE = (CapEx + PV OpEx) / PV Energy
▸ Financial constants: discount rate 6% · project life 30 yr · degradation 0.2%/yr · REC value $0.01/kWh · state industrial rates (EIA 2023, national avg $0.081/kWh).
▸ Viability gate (all three required): NPV > 0 AND payback ≤ 20 yr AND IRR is a real solver result (not a degenerate sentinel).
▸ A 50%-grant NPV scenario is computed alongside (most municipal hydro is grant-supported) — reported but not used for the base viability call.
▸ Design decision (director, Jun 2026): the old $20k/yr minimum-revenue floor was removed — viability is now pure economics. The lever remains in config, reversible with no code change.
WOWERS — Waste Outfall Water Energy Recovery System
11
Notes: [PHASE 4 · METHOD (FINANCE) — the scorecard]
Part two of Phase 4: the financial scorecard. For every sized site we build a thirty-year discounted cash-flow model — "DCF" — which is the standard way to value any infrastructure investment.
The formulas are in the band, but let me translate them. Revenue each year is the energy generated times the state's electricity rate plus a small renewable-energy-credit value — a "REC" is a tradable certificate worth one cent per kilowatt-hour here. Energy declines a tiny 0.2% a year for equipment aging — that's "degradation."
NPV — net present value — is the headline. It's all the future cash flows, each discounted back to today's dollars at a 6% "discount rate," minus the upfront CapEx. The discount rate reflects that a dollar next year is worth less than a dollar today. Positive NPV means the project creates value. IRR — internal rate of return — is the effective annual return rate the project earns; we solve for it numerically. Payback is simply how many years until cumulative savings repay the build cost. And LCOE — levelized cost of energy — is the all-in cost per kilowatt-hour over the project's life, useful to compare against the grid price.
The viability gate requires all three: positive NPV, payback within twenty years, and a real IRR. We also compute a version assuming a 50% grant, since most municipal hydro is grant-supported — reported, but we don't lean on it for the base call.
And a decision you made in June: we removed the old twenty-thousand-dollar minimum-revenue floor, so viability is now pure economics. The lever's still in the config if you want it back.

## Slide 12
PHASE 4 · RESULTS
1,141 investment-ready sites @ 17.5% install
1,141
investment-ready sites
409.1 GWh
annual recoverable energy
9.8 yr
median payback
9.4%
median IRR
CapEx component | $M | Note
Equipment | 181.6 | Power-law, vendor-band clamped
Installation | 31.8 | = equipment × 0.175 (labor)
Interconnection | 82.8 | Tiered by kW
Permitting | 57.3 | FERC conduit / abbrev. / NEPA
Total project CapEx | 353.5 | 4-line sum
Top site | ST | kW | GWh/yr | Pay | IRR
MWRDGC Stickney | IL | 2,644 | 16.9 | 2.1 | 47%
Point Loma WWTP | CA | 1,579 | 10.1 | 2.1 | 48%
AK Warren WRF | CA | 1,192 | 7.6 | 1.1 | 93%
King Co. West Point | WA | 1,136 | 7.3 | 3.7 | 27%
San Jose Creek WRP | CA | 1,111 | 7.1 | 2.2 | 46%
0 of 3,783 sites priced outside vendor bands. 2,642 uneconomic sites are retained (105.6 GWh) with full specs, categorized by payback/NPV/IRR — not discarded.
WOWERS — Waste Outfall Water Energy Recovery System
12
Notes: [PHASE 4 · RESULTS — the headline portfolio]
This is the payoff slide. Of the 3,783 scored sites, 1,141 are investment-ready — meaning, again, positive net present value, payback within twenty years, and a real internal rate of return.
The cards: 1,141 sites, 409 gigawatt-hours per year of recoverable energy, a median payback under ten years, and a median IRR — return — of 9.4%. "Median" means the middle site; half do better. A 9.4% return on infrastructure with sub-ten-year payback is genuinely attractive.
The left table is the total portfolio CapEx — the build cost across all viable sites — broken into the four lines we just discussed: 182 million in equipment, 32 million installation, 83 million interconnection, 57 million permitting, totaling 353.5 million dollars.
The right table is the top five sites by energy. Chicago's Stickney — the biggest plant in the country — would host a 2,644-kilowatt Kaplan turbine, generate nearly 17 gigawatt-hours a year, pay back in two years, at a 47% return. San Diego's Point Loma, 48% return. These are not marginal projects; these are excellent ones.
And the note at the bottom matters for credibility: we do not delete the 2,642 sites that fail economics. They stay in the dataset, with full turbine specs, categorized by profitability. We report everything — we don't cherry-pick and hide the rest.

## Slide 13
THE FUNNEL
How 17,158 POTWs become 1,141 — honestly
Stage | Remaining | Dropped | Why dropped
Phase 1 — ranked POTWs | 17,158 | — | All active POTWs with DMR coverage
Phase 2 — has usable flow | 5,468 | 11,690 | Data gap: no usable EPA flow record
Phase 3 — valid net head | 4,864 | 604 | Data gap: no valid elevation / head
Phase 3 — turbine ≥1 kW | 3,783 | 1,081 | Physics floor: rated power < 1 kW
Phase 4 — investment-ready | 1,141 | 2,642 | Economics: failed NPV / payback / IRR
76.8%
missing data (flow/head) no model could run
6.7%
physics floor <1 kW rated power
16.5%
economics full pro-forma, failed
Headline: ~80% of exclusions are missing public data, NOT economic rejections — the pipeline could not cherry-pick because most sites never reached the financial model. Uneconomic sites are kept, not deleted.
WOWERS — Waste Outfall Water Energy Recovery System
13
Notes: [THE FUNNEL — "how did you exclude everyone else?"]
This is the slide I expect you to push on, so let me address it head-on: how did we get from 17,158 plants down to 1,141? Did we cherry-pick?
Walk down the table. We start at 17,158 ranked plants. After Phase 2, 5,468 remain — we dropped 11,690. After Phase 3 head, 4,864. After turbine sizing, 3,783. After the financial gate, 1,141.
Now here's the key, and it's in the three cards at the bottom. We sorted every exclusion into three reasons. 76.8% of all the drops are missing-data problems — EPA simply had no usable flow record, or the terrain gave no valid head, so we literally could not run any model. 6.7% are a physics floor — the turbine would be under one kilowatt, too small to bother. And only 16.5% are actual economic rejections — cases where we had a complete financial model and the numbers genuinely didn't work.
That structure is the answer to "did you cherry-pick the winners." We couldn't have, because more than three-quarters of the exclusions happened before any financial model was applied — they were excluded by absent public data, not by us choosing favorites. Only one in six exclusions even reached the economics. And as I said, those uneconomic sites aren't deleted; they're kept and categorized.

## Slide 14
PROFIT GRADIENT
Every site graded on 3 economic axes
Payback band | Sites | GWh/yr
Excellent (≤5 yr) | 94 | 181.7
Good (5–10 yr) | 507 | 153.3
Marginal (10–20 yr) | 540 | 74.1
Uneconomic (>20 yr) | 2,642 | 105.6
NPV band | Sites | GWh/yr
High (≥$500k) | 103 | 241.1
Medium ($100–500k) | 155 | 71.9
Low ($0–100k) | 883 | 96.2
Negative (≤$0) | 2,642 | 105.6
IRR band | Sites | GWh/yr
Strong (≥15%) | 196 | 242.1
Moderate (8–15%) | 578 | 120.3
Weak (0–8%) | 2,181 | 139.1
None (<0) | 828 | 13.3
▸ Energy is concentrated: the 94 excellent-payback sites (≤5 yr) hold 182 GWh/yr — ~44% of all viable energy. A pilot targets these first.
▸ The three axes are intentionally independent (e.g. positive-IRR-but-negative-NPV sites land in different buckets) — a richer picture than one binary cut.
▸ 850 of the 1,141 viable sites are also flagged high-confidence (real 3DEP head, not a literature fallback).
WOWERS — Waste Outfall Water Energy Recovery System
14
Notes: [PROFIT GRADIENT — beyond a yes/no]
Rather than just a binary viable-or-not, we grade every scored site on three independent economic dimensions, so you see a gradient, not a cliff. Three tables: payback band, NPV band, and IRR band.
Quick reminders: payback is years to recoup the cost; NPV — net present value — is the dollar value created in today's money; IRR — internal rate of return — is the annual return rate.
Read across. On payback: 94 sites are "excellent" with five years or less, 507 are "good" at five to ten, 540 "marginal" at ten to twenty. On NPV: 103 sites clear half a million dollars of value, another 155 are in the hundred-to-five-hundred-thousand range. On IRR: 196 sites return 15% or more, 578 return eight to fifteen percent.
The strategic takeaway is the concentration. Look at the energy column on the payback table — those 94 excellent sites alone hold 182 gigawatt-hours a year, which is about 44% of all the viable energy. In other words, a small number of outstanding sites carry nearly half the prize. That's exactly where you'd launch a pilot.
The three axes are intentionally independent — a site can have a positive return but still a negative NPV, for instance — which gives a richer picture than one pass-fail line. And 850 of the 1,141 viable sites are also flagged high-confidence, meaning their head came from real elevation data, not a literature fallback.

## Slide 15
TRANSPARENCY
Consolidated assumptions register
Assumption | Value | Basis / note | Lever?
Turbine efficiency η | 0.70 / 0.82 / 0.90 | Triangular; industry range | Phase 2
Availability | 0.90 / 0.95 / 0.98 | Triangular; steady WW flow | Phase 2
Head (no elevation) | by size, 1–15 m | Literature by plant archetype | yes
Head loss fraction | 15% | Pipe friction/valves/bends | yes
Installation cost | 17.5% of equipment | Director 15–20%; labor only | yes ★
Discount rate | 6% | Municipal infrastructure real rate | yes
Project lifetime | 30 years | Standard hydro asset life | yes
Degradation | 0.2%/yr | Hydro output decline | yes
REC value | $0.01/kWh | Conservative certificate value | yes
Electricity rate | state, ~$0.081 avg | EIA 2023 industrial rates | data
Min viable power | 1 kW | Below = not worth a turbine | yes
Min capacity factor | 0.40 | Sizing optimizer constraint | yes
★ = highest leverage on the viable-site count. Every value lives in one file (config/settings.yaml) — the whole pipeline re-runs against a changed assumption with no code edit.
WOWERS — Waste Outfall Water Energy Recovery System
15
Notes: [TRANSPARENCY — the assumptions register]
I want to put every material assumption in one place, openly, so nothing's hidden and you can challenge any single one.
The table lists each assumption, its value, the basis, and whether it's a tunable lever. A few definitions in case they come up: the triangular values like 0.70 / 0.82 / 0.90 are the low, most-likely, and high points of those Monte Carlo distributions. The head loss fraction is the 15% we subtract for pipe friction. The discount rate, 6%, is how we value future dollars. Degradation, 0.2% a year, is equipment aging. The REC value is the renewable-energy-credit price. Capacity factor is the minimum output ratio a turbine must hit to be sized.
The single most important column is the last one — "lever." Almost every assumption can be changed, and the two with the biggest impact on the final site count are starred: the installation cost percentage and the head assumptions.
And here's the part that makes this credible rather than hand-wavy: every one of these values lives in a single configuration file. There's no number buried in the code. If you want to see what happens at a 20% install cost, or a 7% discount rate, we change one line and the entire pipeline re-runs deterministically and gives you the new answer in minutes. So these aren't take-it-or-leave-it assumptions — they're dials you can turn, and we can show you the sensitivity on any of them.

## Slide 16
RIGOR
Why these numbers are defensible
External validation
▸ National P50 = 699 GWh/yr lands inside DOE's independent 500–5,000 GWh/yr range.
▸ Head from real USGS 3DEP terrain, not assumed, on 3,780 sites.
Cost realism
▸ 0 of 3,783 sites priced outside real manufacturer $/kW bands.
▸ Equipment clamped to vendor floors/ceilings (Canyon, Gilkes, CINK, Ossberger).
Engineering quality
▸ 427 automated tests passing (1 skipped) across the Phase 1–4 pipeline.
▸ Per-reading outlier guards removed 459 unit-error artifacts before modeling.
Full reproducibility
▸ Every number traces to a versioned parquet column + a documented formula.
▸ All assumptions in one config; pipeline re-runs deterministically.
WOWERS — Waste Outfall Water Energy Recovery System
16
Notes: [RIGOR — why this is legitimate work]
Let me consolidate why I'd stand behind these numbers, because "a student built a model" deserves scrutiny. Four independent lines of evidence.
First, external validation. Our national energy estimate — that 699-gigawatt-hour central figure — lands inside the Department of Energy's own independent 500-to-5,000 range. And the head on 3,780 sites comes from real USGS terrain data, not assumptions.
Second, cost realism. Zero of 3,783 sites are priced outside the band that real manufacturers — Canyon, Gilkes, CINK, Ossberger — actually publish. The cost model is clamped to reality.
Third, engineering quality. There are 427 automated tests across the Phase 1–4 pipeline, passing. That's not a one-off spreadsheet; it's a tested software system where every calculation is locked down against regressions. And the data is cleaned — those 459 unit-error readings were caught and removed before any modeling.
Fourth, full reproducibility. Every number in this entire deck traces back to a versioned data file and a documented formula. All assumptions are in one config. Anyone can re-run the pipeline and get the identical result.
The point of this slide is simple: this is engineered, tested, auditable work — not a slideware estimate. If you or anyone wants to verify a specific figure, we can take you straight to the file and the line of code that produced it.

## Slide 17
HONESTY
Limitations & caveats
▸ Head is the dominant uncertainty: sensitivity analysis flags head as the #1 NPV driver for ~2,800 of 3,783 sites. Where real 3DEP elevation was unavailable (1,688 sites) we fell back to literature — those are flagged lower-confidence.
▸ Civil works excluded by scope: foundations, trenching, and structural modifications are not in CapEx. The installation line is mechanical labor only. Real-world all-in cost on some sites will be higher.
▸ Energy offset is modest: median viable site offsets ~2% of its own plant electricity load. The pitch is cost savings + sustainability + RECs, not making a plant energy-independent.
▸ Install % is an estimate, not a quote: real government install costs are unobtainable; 17.5% is the director's midpoint proxy. The what-if band (0–20%) swings the count 1,374 → 1,120 sites.
▸ Estimates, not site surveys: this is a national screening tool. Any individual site still needs an engineering site visit before construction.
WOWERS — Waste Outfall Water Energy Recovery System
17
Notes: [HONESTY — limitations and caveats]
I'd rather tell you the limitations than have you find them. There are real ones, and none of them break the result — they scope it.
First, head is the biggest source of uncertainty. Our sensitivity analysis — where we test how much the answer moves when each input moves — flags head as the number-one driver of net present value on about 2,800 of the 3,783 sites. Where we couldn't get real elevation, on 1,688 sites, we used the literature value, and those are flagged lower-confidence.
Second, civil works are deliberately excluded from cost. Foundations, trenching, structural changes — not in our CapEx. The installation line is mechanical labor only. So on some sites the real all-in cost will be higher than we show.
Third, the energy offset is modest. The median viable site offsets only about 2% of its own plant's electricity use. So the honest pitch is operating-cost savings, sustainability, and renewable credits — not making a plant energy-independent.
Fourth, the install percentage is an estimate, not a quote — real government install costs are genuinely unobtainable, so 17.5% is your midpoint proxy. The what-if band swings the site count from 1,374 at zero percent down to 1,120 at twenty percent.
And finally, this is a national screening tool. Any individual site still needs a real engineering site visit before anyone builds anything. We find the candidates; we don't replace the site survey.

## Slide 18
NEXT STEPS
Roadmap & the director ask
THE ASK FOR THE DIRECTOR
Commit the installation % — default 17.5% locks the headline at 1,141 sites / 409 GWh. One config value; reversible. (0% → 1,374 sites; 20% → 1,120.)
▸ Near term: deepen head data — expand real USGS 3DEP coverage to the 1,688 literature-fallback sites; head is the #1 NPV uncertainty, so this sharpens both the viable count and the confidence flags.
▸ Pilot: target the 94 excellent-payback sites (182 GWh/yr) for a concrete, named pilot — the Fowler judges' specific request.
▸ Productize: package the per-site scorecard into the municipality-facing decision tool (which turbine, how much energy, what payback).
WOWERS — Waste Outfall Water Energy Recovery System
18
Notes: [NEXT STEPS — roadmap and the one ask]
Let me close on where we go next and the one thing I need from you — it's in the green box.
The ask: commit the installation cost percentage. The default of 17.5% locks the headline at 1,141 sites and 409 gigawatt-hours. It's a single config value and it's fully reversible. For context, at zero percent it's 1,374 sites; at twenty percent it's 1,120. I just need your committed number so I can finalize the figure we quote externally.
On the roadmap below. Near term, the highest-value technical work is deepening the head data — head is our number-one source of uncertainty, and 1,688 sites are still on a literature estimate rather than real elevation, so expanding real 3DEP coverage directly sharpens both the count and the confidence flags. Then a concrete pilot on the 94 excellent-payback sites — the 182-gigawatt-hour cohort that holds nearly half the viable energy — which is exactly the named pilot strategy the Fowler judges asked for. And finally, we package the per-site scorecard into the municipality-facing tool: tell us your plant, we show you which turbine, how much energy, and what payback.
So: your install number is the one thing that unlocks the finalized headline.

## Slide 19
From public data to a clean-energy portfolio
279M EPA records → 17,158 plants screened → 3,783 turbine-sized → 1,141 investment-ready · 409 GWh/yr
REPRODUCIBILITY — verify any number:
National energy P50
phase2/energy_yield_estimates.parquet
699 GWh/yr
Turbine-viable sites
phase3/turbine_sizing.parquet
3,783
Investment-ready sites
phase4/financial_scorecards.parquet
1,141
Viable energy
phase4 · sum(annual_energy_kwh)
409.1 GWh/yr
Median payback (viable)
phase4 · payback_years.median()
9.84 yr
Portfolio CapEx
phase4 · 4-line sum
$353.5 M
Thank you — questions welcome. WOWERS · University of St. Thomas · Tom Tang & Mohamed Abdel Hamid
Notes: [CLOSING — the one-line summary]
Let me leave you with the one-line version, then open it up.
We go from 279 million public EPA records, to 17,158 plants screened, to 3,783 that we can actually size a turbine for, to 1,141 that are investment-ready — 409 gigawatt-hours per year of recoverable clean energy. And every number on that path is reproducible from a data file and a formula.
The table on this slide is deliberately the audit trail: for each headline figure, the exact output file and the column or calculation that produces it. The national energy estimate, the viable site count, the energy total, the median payback, the portfolio CapEx — point to any one and we can open the file in front of you.
That's the project, beginning to end: where the data comes from, what's in it, how each phase calculates, what came out, and what we assumed. All four phases are production-complete and tested.
I'm happy to go as deep as you want on any phase, any formula, or any assumption. Thank you — what questions do you have?